## Slide 1: CMPE240 Project: The Barkmaster2000 (Keeping dogs entertained since yesterday)
Prepared By:
Bryan Canepa
Patrick Ghorbanian
Sake Dog

## Slide 2: Concept of Design
The Barkmaster2000 encourages your dog to bark
Barkmaster2000 waits in idle state for a bark
If the bark is angry enough it will start spinning
The barkmaster2000 incorporates an IR sensor to detect barking dog
When the IR sensor is triggered the barkmaster will drive forward
Goal is to drive towards the dog to keep her barking

## Slide 3: State Diagram
RESET
Motor Driver Board Init()
SPIN
FORWARD
DRIVE
CLEAR
DATA & STOP
1
IDLE
(Bark < Threshold)
1
(Bark >= Threshold)
_IRsensorCleared
Irsensor
Detect
1
IRsensorCleared
_DETECT
DETECT
1

## Slide 4: Bark Detection
Polls four MEMs audio sensors for input
MEMs inputs provide analog representation of sound
Analog mux used to select MEMs device while in idle state
  GPIO used for addressing mux
Inputs provided to ADC for determination of an “angry bark”
“Angry bark” determined by integrating digitized sound
  Even sampling at 2ms – looking for low frequency to avoid noise
  Adds samples over time and compares to a threshold

## Slide 5: SCHEMATIC

## Slide 6: CUSTOM CIRCUIT BOARDS
MUX & SIGNAL
DISTRIBUTION
BOARD
PIR
SENSOR
BOARD
ULTRASONIC
SENSOR
BOARD

## Slide 7: TOOLS AND 5V REGULATOR BOARD
ASSEMBLY TOOLS
ASSEMBLY TOOLS
5V REGULATOR
BOARD

## Slide 8: TOP VIEW OF THE DIFFERENT LEVELS
TOP VIEW
LEVEL 1
TOP VIEW
LEVEL2

## Slide 9: Challenges
Noise from MEMS sensor was causing issues with bark sensing
  Measured output on scope – lots of high frequency
  Did experiment with different wire lengths showing noise increase
  Used pull-downs within LPC1758 to reduce coupled noise
  Sampled MEMs devices at low frequency (via software) to reduce noise
Acquiring data on a moving object
  Suspected onboard electronics corrupting sound data
  Needed to see sound outputs to debug while Barkmaster2000
  Added Bluetooth capability to get live sampling while operating
Distance sensing
  Original intention was to sense distance and stop if it got too close
  Further testing showed that sensing would limit the movement too much
  More fun to have the Barkmaster2000 just drive right at the dog without stopping
Narrowing the range of the IR sensor
  IR sensor would pick out a 180 degree field
  Taped the exterior of the sensor - small window for sensing
  Not 100% accurate but sufficient to entertain the dog

## Slide 10: The Final Product
Handsome Carrying Tote !!

## Slide 11: Test Subject

## Slide 12: Unleash the Hounds

## Slide 13: Professor’s Name is Virus

## Slide 14: Summary
Barkmaster2000 successfully entertains Bryan’s dog
Hardware incorporates:
  San Jose State processor board
  Analog Mux
  4 MEMs audio sensors
  IR sensor
  On board 5V battery (from 9V source)
  On board motor power
  Ultrasonic distance sensor (disabled for normal operation)
  A squeaky rubber chicken
Utilizes LPC1758:
  PWM motor drive
  ADC inputs for sound sensing
  GPIO for selection of mux channels and IR sensor
  Bluetooth and LED screen for debugging

## Slide 15: The End