## Slide 1: Spread Spectrum Audio Visualizer
By
Jaswanth Bhimanapalli
Sucharitha Sirigireddy
Tianran Chen
Wie Liu

## Slide 2: Agenda
Introduction and Block diagram
Implementation of ADC
FFT integration
LED Matrix initialization (I2C)
Integration testing and bug fixing
Further improvements
Conclusion & Demo

## Slide 3: Block diagram

## Slide 4: Introduction and Block diagram
Fundamental frequency of
  male voice 85 to 180 Hz
  female from 165 to 255 Hz
Audible frequencies 20 Hz to 20 KHz

## Slide 5: Implementation of ADC
Timer 3,Channel 3,12bit
Sampling frequency 8KHz-44.1KHz
Queue to send converted data from ADC
A semaphore to give a sample from ADC to FFT
Test ADC result

## Slide 6: FFT Integration
Cooley-Tukey algorithm for FFT
Takes O(N log N)time to compute FFT on given samples
Project uses 128-point FFT
Modified according to project requirements
Frequency resolution Δf=fs/N
fs=Sampling frequency
N=128
Δf=62.5 Hz
Time interval between samples=1/Δf =0.016 sec
Verified ADC result

## Slide 7: FFT Integration
X[1] represents DC frequency component
X[2] to X[N/2] terms are positive frequency components
X[N/2+1] is the Nyquist frequency (Fs/2Fs/2)
X[N/2+1] to X[N] terms are considered as negative frequency components

## Slide 8: LED Matrix initialization
Standard mode of I2C (100KHz)
Sequence to initialize LED matrix
i2cLED.writeReg(0xE0,0x21,0x00);
i2cLED.writeReg(0xE0,0xA0,0x00);
i2cLED.writeReg(0xE0,0x81,0x00);
Write Data to RAM

## Slide 9: LED Matrix initialization
X – axis for sampling frequency
Y-axis for power spectrum
To fit the samples onto 8 * 8 LED, create bins
X-axis max frequency is 4Khz and displayed in increments of 500 Hz
Y-axis max value is 4096(2*12) and is showing in steps of 512

## Slide 10: Integration testing and bug fixing
Tested each module individually
Integrated ADC with FFT
FFT and LED Matrix
All three modules integrated

## Slide 11: Further improvements
Use bandpass filter at the input
LCD can be used for displaying spectrum

## Slide 12: Conclusion & Demo